## Slide 1: Alphanumeric LCD – AVR ATmega8
Ehsan Yousefzadeh-Asl
2021

## Slide 2: Alphanumeric LCD – How does it work?
LCD stands for Liquid Crystal Display
A peripheral device for displaying data
The reaction of liquid crystal in an electrical field.
Each LCD have a background source of light.
Light goes through liquid crystal.
Electrical fields change the arrangement of the liquid crystal molecules.

## Slide 3: Alphanumeric LCD Characters
A 2*16 LCD shows 32 characters; 16 characters in each row
Every character: a 5x10 or 5x8 or 5x7 matrix of pixels
For showing a character: some of those pixels are on and some of them are off
So, for showing a character, we should send 8 bytes to the LCD
Fortunately, we do not do such things
A controller like HD44780 performs all these tasks and makes microcontroller programmers’ life easy
Row 1: 0-1-1-1-0 / 0x0E
Row 2: 1-0-0-0-1 / 0x11
Row 3: 1-0-0-0-1 / 0x11
Row 4: 1-1-1-1-1 / 0x1F
Row 5: 1-0-0-0-1 / 0x11
Row 6: 1-0-0-0-1 / 0x11
Row 7: 1-0-0-0-1 / 0x11
Row 8: 0-0-0-0-0 / 0x00
Row 1: 1-1-1-1-0 / 0x1E
Row 2: 1-0-0-0-1 / 0x11
Row 3: 1-0-0-0-1 / 0x11
Row 4: 1-1-1-1-0 / 0x1E
Row 5: 1-0-0-0-1 / 0x11
Row 6: 1-0-0-0-1 / 0x11
Row 7: 1-1-1-1-0 / 0x1E
Row 8: 0-0-0-0-0 / 0x00

## Slide 4: Alphanumeric LCD Registers
Every LCD has two registers: Instruction and Data Registers
Instruction Register: Receiving LCD instructions like: Initialization, Screen Clear Command, Cursor location Change Command etc.
Data Register: Receiving the data that will be shown on the LCD

## Slide 5: Alphanumeric LCD Pins

## Slide 6
Pin Number | Pin Name | Description
1 |  | Ground Pin Connected to System Ground.
2 |  | Powers the LCD with +5V
3 |  | Decides the contrast level of display.
4 | RS (Register Select) | Shifts between instruction (0)/ data(1) register.
5 | R/ W (Read/ Write) | Used to read or write data. Grounded (0) to write data to LCD.
6 | E (Enable) | Connected to Micro Pin and toggled between 0 and 1 for data acknowledgment
7 | D0 (Data Pin 0) | These pins form a 8-bit data line. These LCDs can operate on 4-bit mode in which Data Pins 4, 5, 6, and 7 will be left free.
8 | D1 (Data Pin 1) | 
9 | D2 (Data Pin 2) | 
10 | D3 (Data Pin 3) | 
11 | D4 (Data Pin 4) | 
12 | D5 (Data Pin 5) | 
13 | D6 (Data Pin 6) | 
14 | D7 (Data Pin 7) | 
15 | LED Positive | Backlight LED pin positive terminal (Connected to ).
16 | LED Negative | Backlight LED pin negative terminal (Grounded).
Pin Number | Pin Name | Description
1 |  | Ground Pin Connected to System Ground.
2 |  | Powers the LCD with +5V
3 |  | Decides the contrast level of display.
4 | RS (Register Select) | Shifts between instruction (0)/ data(1) register.
5 | R/ W (Read/ Write) | Used to read or write data. Grounded (0) to write data to LCD.
6 | E (Enable) | Connected to Micro Pin and toggled between 0 and 1 for data acknowledgment
7 | D0 (Data Pin 0) | These pins form a 8-bit data line. These LCDs can operate on 4-bit mode in which Data Pins 4, 5, 6, and 7 will be left free.
8 | D1 (Data Pin 1) | 
9 | D2 (Data Pin 2) | 
10 | D3 (Data Pin 3) | 
11 | D4 (Data Pin 4) | 
12 | D5 (Data Pin 5) | 
13 | D6 (Data Pin 6) | 
14 | D7 (Data Pin 7) | 
15 | LED Positive | 
16 | LED Negative | Backlight LED pin negative terminal (Grounded).

## Slide 7: Alphanumeric LCD
E pin on a negative edge, reads from the bus
If the input is data, it will be displayed on LCD
Otherwise, it will be executed
LCD displays have two kinds of RAM memories:
  DDRAM (Display Data RAM): is used for showing ASCII characters – It keeps the hexadecimal data needed for showing each ASCII character on 5x8 matrices
  CGRAM (Character Generator RAM): Enables programmers to build their own customized characters.

## Slide 8: Alphanumeric LCD instructions
In fact, we program the controller of LCD to display what we want
We send instructions to the controller of LCD
We should learn the instructions of the controller of the LCD by reading the controller’s datasheet
 | Instruction Description | Hexadecimal Code of the Instruction
1 | Displaying in 2 rows | 0x38
2 | Displaying in 1 row | 0x30
3 | Displaying in 2 row in 4-bit mode | 0x28
4 | Displaying in 1 row in 4-bit mode | 0x20
5 | Display and RAM clear | 0x08
6 | Display clear without RAM | 0x01
7 | Turning On Cursor and Display | 0x0E
8 | Left Shifting all Content | 0x18
9 | Right Shifting all Content | 0x1C
10 | Left Move of Cursor | 0x10
11 | Right Move of Cursor | 0x14

## Slide 9: LCD Modes
8-bit Mode
  Easier Programming
  Faster Updating of Displayed data
4-bit Mode
  Less pins of the microcontroller are assigned for LCD

## Slide 10: 8-bit Mode
LCD Initialization
0x38
0x01
0x0E
0x80
Displaying in 2 rows
Display clear without RAM
Turning On Cursor and Display
Cursor goes to the first column
of the first row
Sending command 0x38
Delay_ms(1);
Sending command 0x01
Delay_ms(1);
Sending command 0x0E
Delay_ms(1);
Sending Command 0x80

## Slide 11: 8-bit Mode
Sending Commands to LCD
Command Code
RS = 0
R/W = 0
E = 1
Delay
E = 0
PORTB = Command_code;
PORTD = 0x04;
Delay_ms(1);
PORTD = 0x00;
Delay_ms(50);

## Slide 12: 8-bit Mode
Data for Display
ASCII code on Pin
R/W = 0
RS = 1
E = 1
Delay
E = 0
PORTB = character_to_show;
PORTD = 0x05;
Delay_ms(1);
PORTD = 0x00;
Delay_ms(50);

## Slide 13: 4-bit Mode
We can do it with the help of libraries fast and easily.
Functions of alcd library
  Lcd_init(number_of_columns_of_the_LCD)
  Lcd_clear(): removes everything and the cursor goes to location (0,0)
  Lcd_gotoxy(column_number, row_number)
  Lcd_putchar(character_to_display)
  Lcd_puts(string_to_display)